## Slide 1: The Health Benefit and Burden of Mass Donation Programs in Vietnamese Schoolchildren: Impact of Mebendazole
Sam Debaveye1, Claudia Virginia Gonzalez Torres1, Delphine De Smedt2, Bert Heirman3, Shane Kavanagh4, Jo Dewulf1
20/03/2018
1 Research Group Environmental Organic Chemistry and Technology (EnVOC), Faculty of Bioscience Engineering, Ghent University, Campus Coupure, Coupure Links 653, B-9000 Ghent, Belgium
2 Department of Public Health, Ghent University, Campus UZ, De Pintelaan 185, B-9000 Ghent, Belgium
3 Johnson & Johnson EHS&S, Janssen Pharmaceutica NV, Turnhoutseweg 30, B-2340 Beerse, Belgium
4 Health Economics, Janssen Pharmaceutica NV, Turnhoutseweg 30, B-2340 Beerse, Belgium
department OF GREEN CHEMISTRY AND TECHNOLOGY
  research group EnVOC

## Slide 2: The sustainability assessment toolbox today
Source: Dewulf et al., 2016
EC Communication on Integrated Product Policy (COM (2003) 302):
“Life Cycle Assessments provide the best framework for assessing the potential environmental impacts of products currently available”
European Platform for LCA
(EPLCA)
Life Cycle Assessment (LCA):
Policy level:
Notes: [stress difference between environmental life cycle management and the (market) life cycle of a drug]

## Slide 3: Including the benefit of a health care pathway
Patient (Human Health)
Human Health burden in created Disability-Adjusted Life Years (DALYs)
R = Resources
E = Ecosystems
HHbur = Human Health burden
HHben = Human Health benefit
-> DALY as a common metric
to directly compare
Notes: Life Cycle Assessment takes into account three areas of protection: Resources, Ecosystems and Human Health
When considering a health care pathway we can see that this has a measurable positive impact on Human Health for patients
We should account for all Human Health effects
The Human Health benefit can be expressed in DALYs avoided or QALYs gained
The environmental Human Health burden can be expressed in DALYs
We choose DALYs as preferred metric in order to directly compare benefit and burden

## Slide 4: Case study structure: mebendazole Mass Drug Administration
Mebendazole: production data available from Janssen Pharmaceutica
Environmental Life Cycle Assessment -> Global Human Health burden
Markov model to estimate treatment effect -> Patient Human Health benefit
Comparison between burden and benefit
Conclusions
Notes: We performed a cradle-to-grave case study on mebendazole mass donation in Vietnam
Patients suffer from anaemia, wasting, abdominopelvic problems, … Deworming can be achieved with medication
As re-infection occurs within months, it is necessary to maintain treatment
We will compare 2 scenarios: 6-monthly treatment of mebendazole with No Treatment
The study focuses on Vietnamese school-aged children, so Vietnamese data for children was used where possible
First I will discuss the Life Cycle Assessment of the pharmaceutical supply chain, to model the Human Health burden
Then I will discuss the Markov model approach to model the Human Health benefit

## Slide 5: Case study: mebendazole Mass Drug Administration
Disease area: Soil-Transmitted Helminthiases
  Three main worm infections: Hookworm, Ascaris lumbricoides and Trichuris trichiura
  Patients suffer from anaemia, wasting, abdominopelvic problems, …
  Reduction in worm burden achieved with anthelmintic medication
  Re-infection often occurs within months
Notes: We performed a cradle-to-grave case study on mebendazole mass donation in Vietnam
Patients suffer from anaemia, wasting, abdominopelvic problems, … Deworming can be achieved with medication
As re-infection occurs within months, it is necessary to maintain treatment
We will compare 2 scenarios: 6-monthly treatment of mebendazole with No Treatment
The study focuses on Vietnamese school-aged children, so Vietnamese data for children was used where possible
First I will discuss the Life Cycle Assessment of the pharmaceutical supply chain, to model the Human Health burden
Then I will discuss the Markov model approach to model the Human Health benefit

## Slide 6: Case study: mebendazole Mass Drug Administration
Comparison of 2 scenarios
  Anthelmintic mebendazole 500 mg 2x/year treatment (WHO regimen)
  No Treatment
Time horizon: 2006-2011
Target: 13 million Vietnamese school-aged children (5-14y), reaching 80% coverage
WHO 2012. Eliminating Soil-Transmitted Helminthiases as a public health problem in children: progress report 2001-2010 and strategic plan 2011-2020. Geneva
Notes: We performed a cradle-to-grave case study on mebendazole mass donation in Vietnam
Patients suffer from anaemia, wasting, abdominopelvic problems, … Deworming can be achieved with medication
As re-infection occurs within months, it is necessary to maintain treatment
We will compare 2 scenarios: 6-monthly treatment of mebendazole with No Treatment
The study focuses on Vietnamese school-aged children, so Vietnamese data for children was used where possible
First I will discuss the Life Cycle Assessment of the pharmaceutical supply chain, to model the Human Health burden
Then I will discuss the Markov model approach to model the Human Health benefit

## Slide 7: Environmental Life Cycle Assessment - Human Health burden
Data: Janssen Pharmaceutica supply chain
Includes full cradle-to-grave assessment of pharmaceutical supply chain
Envelops:
- Excretion of mebendazole molecule into the environment
- Packaging waste
Data: National Institute of Malariology, Parasitology and Entomology, Vietnam
Notes: In the LCA we included the full cradle-to-grave impact of the pharmaceutical supply chain
All production and supply stages of the medication are included: the synthesis of the Active Pharmaceutical Ingredient, the formulation of the tablet, the packaging, the distribution and the End-of-Life of both the active molecule and the packaging materials.
The Drug Administration is also included in this figure but we did not consider any resource use for that stage
We obtained data from multiple sites within the Janssen Pharmaceutica supply chain and also from the national institute of malariology, parasitology and entomology in Vietnam
In that way we have primary data for all stages of the pharmaceutical supply chain
The environmental impact was calculated through internationally accepted software packages and databases

## Slide 8: Environmental Life Cycle Assessment - Human Health burden
e.g. kg CO2-equivalents
Δ°C incr. / kg CO2-eq
DALY / Δ°C incr.
(malnutrition,diseases, …)
Notes: In the LCA we included the full cradle-to-grave impact of the pharmaceutical supply chain
All production and supply stages of the medication are included: the synthesis of the Active Pharmaceutical Ingredient, the formulation of the tablet, the packaging, the distribution and the End-of-Life of both the active molecule and the packaging materials.
The Drug Administration is also included in this figure but we did not consider any resource use for that stage
We obtained data from multiple sites within the Janssen Pharmaceutica supply chain and also from the national institute of malariology, parasitology and entomology in Vietnam
In that way we have primary data for all stages of the pharmaceutical supply chain
The environmental impact was calculated through internationally accepted software packages and databases

## Slide 9: Results: Global Human Health burden - DALYs created
Chart: DALY
| API Synthesis | Formulation | Packaging | Distribution & Supply | End-of-Life
Chemicals & Water | 4.8226 | 0.056117 | 0 | 0 | 0
Energy | 4.137 | 1.1548 | 0.017687 | 0 | 0
Packaging | 0 | 0 | 0.068384 | 0 | 0
Waste | 0.059241 | 0.019904 | 0 | 0 | 0.006455
Transport | 0.058763 | 0 | 0 | 0.10386 | 0
Mebendazole 2x/year for 13 M children for five years
10.5 DALYs associated with pharmaceutical supply chain
Notes: When treating 13 million Vietnamese children every six months for five years, 10.5 DALYs are created because of environmental emissions of the pharmaceutical supply chain
When looking into more detail, we can see that the chemical synthesis of the molecule is responsible for the highest burden, mainly due to the use of chemicals, water and energy
The formulation of the tablet has the second highest impact
The packaging, distribution and End-of-Life phases have negligible environmental impacts

## Slide 10: Markov model structure – Hookworm example
Montresor, A., et al. 2013. Trans R Soc Trop Med Hyg 107 (5), 313-318.
Pullan, R. L., et al. 2014. Parasit Vectors 7 (1), 1-19.
One-year cycles
Disability is multifactorial
Key drivers listed
Disability:
Disability:
Disability:
Notes: We adopted and modified an existing Markov model, published by Antonio Montresor, to calculate STH prevalence over time
Each health state has a specific disability, dependent on the intensity of infection. The disabilities were adopted from the Global Burden of Disease
The model has cycles of one year
Patient can move throughout the model states each year on a population level
As children are treated, the prevalence in the moderate and heavy infections will go down
Mention added value of own adaptations of the model

## Slide 11: Calculation of disability
Based on literature review for all disabilities
Disability weights from Global Burden of Disease 2013
Focus on anaemia: responsible for largest disability fraction
Total Hookworm prevalence varies, but relative prevalence anaemia by intensity are assumed constant
0.149
(moderate)
(severe)
Disability:
0.004
0.052
(mild)
×
×
×
E.g. at model start: 8M children with hookworm light infection
Mild anaemia: 8M x 42.07% x 0.004 = 14.000 DALYs
Notes: We quantified the disability due to anaemia by subdividing the total anaemia prevalence into mild, moderate and severe anaemia for each intensity of Hookworm infection
Simplifying assumption: the % of anaemia is kept constant but the prevalence is reduced over time
The prevalence was then multiplied with the disability for each intensity of anaemia
As the prevalence of Hookworm goes down after multiple rounds of treatment, the prevalence of anaemia and the disability also drops

## Slide 12: Results: Patient Human Health benefit - DALYs avoided
Mebendazole 2x/year for 13 M children for five years, compared to No Treatment
Chart: DALY
| Hookworm | A. lumbricoides | T. trichiura
No Treatment | 171780.7981 | 40206.9634 | 29977.902
Mebendazole | 27822.1289 | 6177.5 | 3714.8983
84% reduction
85% reduction
88% reduction
144,000 DALYs avoided
+34,000 DALYs avoided
+26,000 DALYs avoided
=204,000 DALYs avoided
No. infected
  2.5 M → 500,000
  3.7 M → 1 M
10 M → 2 M
Notes: When looking at the patient Human Health effect, the burden of Soil-Transmitted Helminthiases drops on average 85% for all three worms
For Hookworm, 144,000 DALYs are avoided, no. infected from 10 million to 2 million
For Ascaris 34,000 DALYs are avoided, no. infected from 2.5 million to 500.000
And for Trichuris 26,000 DALYs are avoided, no. infected from 3.7 million to 1 million
That results in a total of 204,000 DALYs avoided

## Slide 13: Comparison between benefit and burden
Patient health benefit outweighs burden
  Factor 19,000
Treatment
Global
Human Health
burden (DALY)
Increment
Human
Health
benefit (DALY)
Increment
No Treatment
0.00
242,000
Mebendazole
10.50
+
10.50
38,000
–
204,000
85%)
(–
Patient
Notes: If we compare both the Human Health benefit and burden of the treatment, we can see that the Human Health burden with 10.5 DALYs created is vastly outweighed by the Human Health benefit, with 204,000 DALYs avoided.
The Human Health benefit is a factor 19,000 larger than the Human Health burden

## Slide 14: Conclusions
API synthesis causes highest environmental burden
Modelling WHO anthelmintic regimen: an estimated 85% DALY improvement during five years treatment
Treatment reduces total Human Health burden
  DALY medication
  DALY patients
New methodology to assess Mass Drug Administration programs: patient health benefit may outweigh environmental burden in health care
→ 19,000 times more DALYs avoided than created
Notes: As first conclusion of this study we can say that API synthesis causes the highest environmental burden in the pharmaceutical supply chain of mebendazole
The improved Markov model developed for this study estimates that 85% of disability is improved over five years of treatment
When comparing both benefit and burden it is clear that the treatment avoids DALYs because the added burden due to medication is outweighed by the reduction in burden of the patients
These are the first results of a new methodology to assess the combined Human Health performance of donation programs on the patient and the environment. The results indicate that the patient health benefit may significantly outweigh the environmentl burden

## Slide 15: Thank you! For additional info contact:
Sam Debaveye Sam.Debaveye@UGent.be VLAIO, Baekeland mandate grant no. 140249
department OF GREEN CHEMISTRY AND TECHNOLOGY
  research group EnVOC

## Slide 16: Improved Markov model structure and progression
STH total prevalence at year 0:
76% 19% 29%
63.39%
8.32%
4.29%
13.89%
4.79%
0.32%
24.95%
3.97%
0.09%
Input for next model cycle of 1 year
Treatment
Notes: We start from a general STH prevalence from before the introduction of mass deworming
This total prevalence is subdivided into three levels of infection
Then the model runs one cycle, after which the prevalences of each intensity are summed to a total prevalence per worm
Then the total prevalence is subdivided again into three levels of infection with the same formula as the first subdivision, which allows a more stable set of disability calculations
By calculating the disability each year for 5 years, we can compare the treatment No Treatment

## Slide 17: Disclosure of competing financial interests
Shane Kavanagh and Bert Heirman are employees of Janssen Pharmaceutica, an operating company of Johnson & Johnson and also hold stock and options in Johnson & Johnson
This work was carried out as part of a PhD program jointly funded by the Flemish government (Flemish Innovation and Entrepreneurship, VLAIO) and Janssen Pharmaceutica as a Baekeland mandate grant (no. 140249) of Sam Debaveye
Sam Debaveye received travel funding through the Baekeland mandate grant
Jo Dewulf worked as a consultant for Janssen Pharmaceutica
Delphine De Smedt and Claudia Virginia Gonzalez Torres declare no actual or potential competing financial interests